# Description of an M-Lab site

Description of an M-Lab site

Site architecture

Switch Port Assignments

Servers, DRACs, switch names

Full list of equipment

## Site architecture

An individual M-Lab site comprises 4 devices: 3 servers and 1 switch.

The servers are managed remotely (in the case of the Dells) with a “DRAC” card which is independently cabled to the switch.

The switch can be configured as a router or just a switch - in both cases the switch is used to the connect the servers to the Internet (eg. via a /30 subnet to an ISP).

See a diagram of an M-Lab site at https://docs.google.com/a/google.com/viewer?a=v&pid=sites-dogfood&srcid=Z29vZ2xlLmNvbXxtLWxhYnxneDozNDJlYWNkMDMyNjc1OWY5.

## Switch Port Assignments

- 24 port switch:

  - 1G Transit:  Port 24

  - MLAB1, Ethernet:  Port 1

  - MLAB1, DRAC:  Port 3

  - MLAB2, Ethernet:  Port 5

  - MLAB2, DRAC:  Port 7

  - MLAB3, Ethernet:  Port 13

  - MLAB3, DRAC:  Port 15

- 48 port switch:

  - 1G Transit:  Port 48

  - MLAB1, Ethernet:  Port 1

  - MLAB1, DRAC:  Port 3

  - MLAB2, Ethernet:  Port 13

  - MLAB2, DRAC:  Port 15

  - MLAB3, Ethernet:  Port 25

  - MLAB3, DRAC:  Port 27

## Servers, DRACs, switch names

- Server FQDNs:

  - mlab1.<site name>.measurement-lab.org

  - mlab2.<site name>.measurement-lab.org

  - mlab3.<site name>.measurement-lab.org

- DRAC FQDNs:

  - mlab1d.<site name>.measurement-lab.org

  - mlab2d.<site name>.measurement-lab.org

  - mlab3d.<site name>.measurement-lab.org

- Switch FQDN

  - s1.<site name>.measurement-lab.org

## Full list of equipment

- Servers.

  - 3 x DELL PowerEdge R610, 1U, 2x Xeon E5606 2.13GHz, 8x1GB 1333MHz UDIMM, 2x 250GB SATA 7.2K 2.5in Hotplug HDDs, SAS 6/iR, iDRAC6 Enterprise, 1x 502W PSU, 2x Dual-Port 1GbE PCIe-4 NICs w/TOE iSCSI, DVDROM, 6x2.5in Chassis, Custom.

  - 3 x DRAC module (iDRAC6 Enterprise RJ-45 port) - Either ships separately or comes installed in the server.

  - 3 x Rack mount kit. (normally ships separately).

  - OPTIONAL 6 x extension brackets. -- They are site-dependent (site with non adjustable rails will require extension bracket for good installation).

- Dedicated switch with at least read-only SNMP v2 access.

  - 1 x HP Procurve 2848, 48 ports, 10/100/1000Base-T, 1U.

  - The switch must be running at least version I.10.70.

- Network cables (check length)

  - 1 x HP, GIGABIT LX-LC MINI-GBIC J4859C (note that this is single-mode).

  - 6 x yellow cat5 patch w/ approved rj45 (3 for regular LAN interfaces, 3 for DRACs).

  - 1 x CBL, PATCH FIBER SM, SC-LC DX (fiber cable, single-mode, SC-LC for the uplink 1G connection)

- Power cords (check length and other site-specific power requirements)

  - 1 x Servertech Horizontal Power Strip (8port) MASTER.

  - 4 x 6FT UNIV AC POWER COMPUTER EXTENSION MALE/FEMALE - c13 to c14 (For Servertech) - connection to devices.

  - 1 x Power Cord, C19 to IEC 60309, (15') - connection to commando sockets.

# Comments

tiziana:

TODO: Create more clear diagram.